## Slide 1
引言逻辑闭环：从真实飞行到可用仿真模型
核心问题：如何把真实飞行日志中的 effective wrench 转化为可解释、可验证、可用于仿真的气动模型修正？
1
真实扑翼飞行日志
户外飞行
控制、状态、相位、空速
2
重构 effective wrench
非重力外力/力矩
面向仿真
3
解析气动先验
calibrated DeLaurier
force prior
4
发现模型残差
phase / frequency
condition structure
5
通道感知混合模型
force: prior + residual
moment: direct head
6
仿真验证目标
短窗口 rollout
局部动力学一致性
residual diagnosis guides model repair
核心主张
不是 NN 替代物理模型，而是用真实飞行 residual 诊断并修正物理先验的适用边界。

## Slide 2
论文内容组织：问题定义 → 模型 → 诊断 → 验证
一条主线：真实飞行 effective wrench 作为目标，DeLaurier force prior 作为结构，residual 诊断指导模型修正。
1
问题与数据
真实飞行日志
effective wrench label
2
物理先验校准
DeLaurier-style force prior
training-only calibration
3
主模型设计
force-prior + residual Transformer
moment-direct head
4
模型对比实验
prior / direct NN
full-wrench residual / force3
5
残差结构分析
phase bins
frequency energy
condition bins
6
解释性 grey-box
low-order harmonic correction
partial residual closure
7
仿真相关验证
short-horizon rollout
local consistency
实验纪律
whole-log split
date-stratified 5-fold
no acceleration leakage
held-out reporting
论文结论
解析模型提供可解释 force prior；真实 effective moment 需单独处理；residual 具有可诊断结构，可指导仿真模型修正。